## Slide 1: High-Performance Heterogeneous Computing for Genomics Applications Dept. of Computer Science and Engineering University of South Carolina
Dr. Jason D. Bakos
Associate Professor
Heterogeneous and Reconfigurable Computing Lab (HeRC)
This material is based upon work supported by the National Science Foundation under Grant Nos. CCF-0844951 and CCF-0915608.
CUNY NSF Workshop on Accelerators in High Performance Computing
Center for the Arts, College of Staten Island
June 5-6, 2012

## Slide 2: Lab Objectives
Implement and evaluate various scientific applications on heterogeneous platforms
  Emphasis on non-mainstream coprocessor types
    FPGA, DSP, some GPU
  Emphasis on new applications
    Non-regular grid
Use experience to develop development tools and methodologies

## Slide 3: Application Areas
Comparative genomics:
  GRAPPA: Gene Rearrangement Analysis under Parsimony and other Phylogenetic Algorithms (FPGA)
  MrBayes/BEAGLE: Sequence based phylogeny reconstruction (FPGA)
Metagenomics:
  Pyrosequencing noise removal (GPU)
Data mining:
  Frequent itemset mining (FPGA/GPU)
  Clustering (GPU)
Lossless compression:
  Logic optimization based compression (GPU)
Sparse linear algebra:
  Sparse matrix-vector multiply (FPGA)
  Streaming reduction architectures (FPGA)

## Slide 4: Platforms
Annapolis Micro Systems WILD STAR II Pro:
  One Xilinx Virtex-2 Pro 100 (100K gates at 50 MHz)
  2 GB/s SRAM b/w
  PCI-X host interface

## Slide 5: Convey HC-1
Large coprocessor board with FSB interface to host
  FSB interface keeps coprocessor memory coherent with host
Four Xilinx-5 LX 330s
  ~1.32M gates at 150 MHz
Memory is partitioned into eight disjoint regions
  Each FPGA has a channel to each of these regions
  Max bandwidth 76.8 GB/s
  16 GB memory
Compared with WILDSTAR:
  13.2 X FPGA resources
  28.4 X memory bandwidth
  >1000X memory capacity

## Slide 6: GiDEL PROCSTAR III
8-lane PCIe Gen.2 8-lane
Four Altera Stratix 260 FPGAs
  1.04M gates at 250 MHz
  Each FPGA has three 64-bit DDR2 memories
    4 GB/s on board DRAM / 4 GB/s SODIMM / 2.1 GB/s SODIMM
    Aggregate bandwidth 40.4 GB/s
    16 GB memory

## Slide 7: Genomics Applications
GRAPPA [phylogenetic inference]
  Instead of sequences of nucleotides, uses gene order data
  Infer evolutionary relationships through gene rearrangement events
  Relies on combinatorial search
MrBayes / BEAGLE-Lib [phylogenetic inference]
  Traditional sequence-based data
  Operates on floating-point vectors
  Widely used
AmpliconNoise [metagenomics]
  Metagenomics (analysis of mixed DNA)
  Reads large set of short reads from 454 sequencer
  Objective: remove noise that overestimates # of species
  Relies on alignments and clustering

## Slide 8: Phylogeny Reconstruction
Evolutionary relatedness among set of input species
Given input species, find accurate evolutionary history

## Slide 9: Phylogenies
Possible binary trees with n leaves:
  (2n - 5) * (2n - 7) * (2n - 9) * … * 3
  16 leaves => 200 trillion trees
  50 leaves => 2.8e74 trees (250 = 1.1e15)
Phylogeny reconstruction tools search tree space for most accurate tree
  Basic algorithm:
  Explore space of all possible trees
  When a candidate tree is found, score it
  Involves computing ancestral data

## Slide 10: GRAPPA: Gene Order Data
Each gene represents a homologous nucleotide sequence
  Each gene has a positive or negative orientation
Based on the evolutionary model of gene rearrangements:
  Inversion
    g0 g1 g2 g3 g4 g5 g0 g1 –g4 –g3 –g2 g5
  Transposition
    g0 g1 g2 g3 g4 g5 g0 g2 g3 g4 g1 g5
Compared with DNA sequences, gene orders are relatively short
  Goal:
    Directly estimate ancestral gene orders
    Determine number of events along branches in tree

## Slide 11: GRAPPA: Median Computation
Each candidate tree: label internal vertices with a median gene order
Find M that optimally minimizes median score
score = d(A,M) + d(B,M) + d(C,M)
Is computational kernel for data sets with high evolution rate

## Slide 12: GRAPPA: Breakpoint Median Algorithm
A = -1 +2 -4 -3
B = -1 -2 +3 +4
C = -2 +3 +4 +1
Decompose to edges:
-3,4 weight 0
2,3 weight 1
-1,-2 weight 2
1,2 weight 2
-1,-4 weight 2
1,-4 weight 2
-2,-4 weight 2
+
-
+
+
+
-
-
-
1
2
4
3
Edges not shown have cost = 3
weight = -¥
weight = 0
weight = 1
weight = 2
+
-
+
+
+
-
-
-
1
2
4
3
An optimal solution corresponding to genome +1 +2 -3 -4
Input gene orders => graph
Perform TSP, tour corresponds to median

## Slide 13: GRAPPA: Hardware Median Core Design
Perform DFS to find every valid combination of edges
For each partial search state, perform lower bound computation
  Requires traversal of edge list
  Greedily add edges to complete tour
  Exclude edges that were pruned in partial state or that would cause cycle
Imp. as controller and on-chip RAMs
  No off-chip memory access

## Slide 14: GRAPPA: Parallelizing Median
Processing elements are compact
Fine-grain
  Replicate onboard RAMs by lower bound by factor of 20X
  Perform 20 iterations of lower bound loop in parallel
Coarse-grain
  Use multiple median cores for single median computation
  Each core uses different ordering of same-weighted edges in edge list

## Slide 15: GRAPPA: Median Acceleration Performance
Average Events per Edge | Average Median Speedup
19 | 22
20 | 45
21 | 52
22 | 91
23 | 136
24 | 154
25 | 876
Average Events per Edge | Average Application Speedup
10 | 6
11 | 9
12 | 129
13 | 189
Median performance:
Application performance:

## Slide 16: GRAPPA: Branch and Bound for Trees
Also developed PE for bounded DFS search for tree space
Lower bound = F(leaf ordering)
Implement as processing element as FSM controller and on-chip RAMS
  FPGA can fit 37 PE instances
Equally divide search space among multiple processing elements

## Slide 17: GRAPPA: Tree Generation Performance
Leaves | Trees | Speedup w/1PE | Speedup w/8PEs | Speedup w/16PEs | Speedup w/20PEs
10 | 2e6 | 2 | 7 (x3.6) | 8 (x4.4) | 8 (x4.4)
11 | 3e7 | 3 | 16 (x5.0) | 23 (x7.2) | 23 (x7.3)
12 | 7e8 | 3 | 18 (x5.2) | 26 (x7.8) | 26 (x7.6)
13 | 1e10 | 4 | 19 (x5.5) | 28 (x8.4) | 28 (x8.0)
14 | 3e11 | 5 | 25 (x5.6) | 37 (x8.6) | 37 (x8.2)

## Slide 18: MrBayes: Likelihood-Based Inference
Uses DNA data (A,C,G,T)
Represent each character as a likelihood of being A, C, G, or T
  At leaves: 4-value vector for each character:
  A, G, A, C, A, T =>
  (1,0,0,0), (0,0,1,0), (1,0,0,0), (0,1,0,0), (1,0,0,0), (0,0,0,1), …
  Internal nodes, calculate each character as non-zero likelihoods:
  (0.3, 0.1, 0.4, 0.2), …
To score candidate, traverse all nodes from leaves to root:
  Calculate likelihoods for internal nodes as a function of left and right decedents
  At root: calculate tree likelihood
    Accumulate log of the maximum likelihood for each character

## Slide 19: MrBayes: Likelihood-Based Inference
P
L
R
 | A | C | G | T
1 |  |  |  | 
2 |  |  |  | 
3 |  |  |  | 
 | A | C | G | T
1 | .24 | .65 | .10 | .01
2 | .31 | .15 | .32 | .22
3 | .11 | .21 | .38 | .30
 | A | C | G | T
1 | 0 | 1 | 0 | 0
2 | 1 | 0 | 0 | 0
3 | 0 | 0 | 1 | 0
clL
clR
leaf
 | A | C | G | T
A |  |  |  | 
C |  |  |  | 
G |  |  |  | 
T |  |  |  | 
tipL
 | A | C | G | T
A |  |  |  | 
C |  |  |  | 
G |  |  |  | 
T |  |  |  | 
tipR
clP[A]=(clL[A]*tipL[AA] + clL[C]*tipL[AC]
+ clL[G]*tipL[AG] + clL[T]*tipL[AT])
* (clR[A]*tipR[AA] + clR[C]*tipR[AC]
+ clR[G]*tipR[AG] + clR[T]*tipR[AT])
clP[C]=…
clP

## Slide 20: MrBayes: High Level Synthesis
Requires many operators but no dependences between indices
  Requires 10 inputs and generates 6 outputs per “loop iteration”
  Performs 130 FP operations per 64 bytes of I/O
    Includes polynomial log approximation
  38 adds, 55 multiplies, 4 divides, 11 comparisons
  Arithmetic intensity = 2.03 flops/byte [memory bandwidth bound]
On Convey HC-1:
  Eight independent memory channels on each FPGA
  Associate one FP pipeline per channel
  Each channel can supply four input values per cycle
    Data Introduction Interval (DII) = 10/4 = 3 cycles
    Set port constraint
  GOAL: assume peak b/w, instance minimal # of FUs = # ops / DII
None of our commercial HLS tools would do this
Developed a port constrained high-level synthesis tool

## Slide 21: MrBayes: Port Constrained Synthesis
Objective: for memory-bound kernels…
  Generate pipeline having throughput match available input bandwidth
  Minimize # functional units, lower bound = # ops / DII
  Minimize overhead (muxes and registers) from FU sharing
Algorithm:
  Input: DFG of kernel
  Instance minimal # of functional units of each type
  Loop:
    Choose a DFG operator whose inputs have already been scheduled
    Attempt to schedule it as early as possible
    If there aren’t enough instanced functional units, move it forward in the schedule until there are no conflicts

## Slide 22: MrBayes: Functional Unit Sharing
Expanded Phylogenetic Likelihood Function for one base:
clP[h] = (tipL[AA]*clL[A] + tipL[AC]*clL[C] +
tipL[AG]*clL[G] + tipL[AT]*clL[T]) * (tipR[AA]*clR[A] + tipR[AC]*clR[C] + tipR[AG]*clR[G] + tipR[AT]*clR[T]);
DFG
Cal. DII, min. FUs
Schedule FU with heuristic
Node | Slot | Type | FU
1 | 1 | × | mul1
2 | 2 | × | mul1
3 | 3 | × | mul1
4 | 4 | × | mul1
5 | 5 | × | mul1
6 | 6 | × | mul1
7 | 7 | × | mul1
8 | 8 | × | mul1
9 | 10 | + | add1
10 | 12 | + | add1
11 | 14 | + | add1
12 | 16 | + | add1
13 | 25 | + | add1
14 | 29 | + | add1
15 | 42 | × | mul2
user
+ port constraints

## Slide 23: MrBayes: Data Flow Graph
Natural log approximation:
order-5 polynomial (Chebychev)

## Slide 24: Design
Instance 8 pipelines per FPGA = 32 pipelines
In order to get likelihood logic to fit:
  Leverage relatively slow clock of HC-1 to reduce latency of FUs:
  3-cycle FP add, 3-cycle FP mult [DSP], 11-cycle FP divide
Final design with 8 PEs/FPGA:
  93% LUT, 96% FF, 99% slice, 81% BRAM, 79% DSP
Performance potential
  2.03 flops/byte x 76.8 GB/s x memory efficiency
  50% memory efficiency => 78 GFLOPS/s
Performance results:
  3X speedup vs. BEAGLE on Tesla T10 GPU
  50X speedup vs. BEAGLE on dual 4-core Xeon 5520

## Slide 25: Port Constrained Synthesis of FP Pipelines
Applied tool to SBML rate law (ODE) benchmark expressions
Example:
  PPBR
  13 inputs, 8 adds, 12 multiplies, 5 divides
  Assume DII = 5
  Evaluate compared with exhaustive search (w/1-cycle add, 2-cycle mult, 4-cycle divider):
    Pipeline latency (min,max)=(31,34), our result=31
    Maximum fanin (min,max)=(4,5), our result=5
    Maximum fanout (min,max)=(4,6), our result=5
    # muxes (min,max)=(48,76), our result=61
    # registers (min,max)=(25,48), our result=26

## Slide 26: Comparison with Commercial HLS Tools
For same benchmark:
  Assume border case with one physical input port, DII=13
  Evaluating AutoESL now
 | ImpulseC | SynforaC | Our tool
FUs | 25 | 7 | 3
Total LUTs | 6605 | 4805 | 2236
Total regs | 6453 | 4066 | 1820
Speed | 150.2 MHz | 146.8 MHz | 158.MHz

## Slide 27: AmpliconNoise: Pyrosequencing Noise Removal
In metagenomics, sequence mixed genomes from different bacterial species
Goal: remove noise to prevent overestimation of # unique genomes
Roche 454 sequencer
Produces a run of
~100K short reads of ~800 length each
Kernel:
  Cluster reads to differentiate unique species
  Compute pairwise distance matrix
  Distances based on global alignment score

## Slide 28: AmpliconNoise: Global Alignment
sequence 1: A G G T C C A G C A T
edits:
A C C T A G C C A G C A T
insert
change
delete
Aligned sequence 1: A G G T - - C C A G C A T
Aligned sequence 2: A C C T A G C C A - - A T
A C C T A G C C A A T
sequence 2:
Match similar sequences to each other
  Alignment “uncovers” edits (gaps show deletions/insertions):

## Slide 29: AmpliconNoise: Score Matrix
Basic idea:
  Based on penalties for:
    Adding gaps to sequence 1
    Adding gaps to sequence 2
    Character substitutions (based on table)
  Construct a score matrix, where:
    Each cell (i,j) represents score for a partial alignment state
A | B
C | D
D = best score, among:
  Add gap to sequence 1 from B state
  Add gap to sequence 2 from C state
  Substitute from A state
Final score is in lower-right cell
Sequence 1
Sequence 2

## Slide 30: AmpliconNoise: Global Alignment
Also need to compute move matrix, which records which option was chosen for each cell
Trace back to get for alignment length
AmpliconNoise: Divide score by alignment length
 | A | G | G | T | C | C | A | G | C | A | T | 
A | D | L | L | L | L | L | L | L | L | L | L | L
C | U | D | D | L | L | L | L | L | L | L | L | L
C | U | U | D | D | D | L | L | L | L | L | L | L
T | U | U | D | D | D | D | L | L | L | L | L | L
A | U | U | U | D | D | D | L | L | L | L | L | L
G | U | U | U | U | U | U | L | L | L | L | L | L
C | U | U | U | U | U | U | D | L | L | L | L | L
C | U | U | U | U | D | D | D | D | L | L | L | L
A | U | U | U | U | U | D | D | D | L | L | L | L
A | U | U | U | U | U | D | D | D | L | L | D | L
T | U | U | U | U | U | U | U | D | L | L | D | D
 | U | U | U | U | U | U | U | U | U | D | D | D
match
match
gap s1
gap s1
match
match
match
gap s2
gap s2
match
substitute
substitute
match

## Slide 31: Accelerating AmpliconNoise with GPU
Most previous work:
  Assumes local alignment for database search
    One large alignment at a time
  Associate one thread with each cell in each diagonal of score matrix
Our approach:
  Billions of small alignments
  One thread to each alignment operation
  Interleave sequence data to ensure coalesced loads
  Also:
    Store substitution matrix in shared memory
    Used performance testing to find optimal number of threads

## Slide 32: AmpliconNoise: Performance Results
3 Fermi GPUs achieves 18.3X speedup over 12 threads on Sandy Bridge CPU
3 GPUs achieves equivalent performance to 216 MPI ranks
  (18 nodes with 12-thread CPUs)

## Slide 33: Conclusions
FPGA and GPU coprocessors are a good match for demanding applications and datasets in genomics
Better development tools and methodologies are needed, especially for FPGA-based coprocessors
In particular, system simulators are needed that incorporate host-coprocessor interconnect models and coprocessor memory models needed for design space exploration