## Slide 1: Accuracy, Cost, and Performance Trade-offs for Floating Point Accumulation
Krishna K. Nagar and Jason D. Bakos
Univ. of South Carolina

## Slide 2: Floating Point Accumulation
Problem:
  For floating point accumulation, high throughput and high accuracy are competing design goals
Motivation:
  Fully pipelined, streaming d.p. f.p. accumulator
  Accepts one new value and set ID on every clock cycle
  Exploits parallelism both within and across accumulation sets
  Based on dynamically scheduling inputs to a single floating point adder
  However, accuracy was inconsistent and data dependent
ReConFig 2013 Ph.D. Forum 2

## Slide 3: High Throughput Accumulation
d1
Asum
c1
c3
c2
Bsum
Dynamically schedule:
  Adder inputs
  Next input value
  Output of adder
…based on datapath priorities and the set IDs
Accumulator Input
Buffers
Adder Pipeline
ReConFig 2013 Ph.D. Forum 3
?
?
?
?

## Slide 4: Accumulator Design
d1
Asum
c1
c3
c2
Bsum
d2
Bsum
c2+c3
d1
c1
Rule 2
Rule 4
ReConFig 2013 Ph.D. Forum 4

## Slide 5: Accumulator Design
d4
c2+c3
d3
c1
d1+d2
d3
c1
D1+d2
C2+c3
Rule 5
Rule 1
ReConFig 2013 Ph.D. Forum 5
0

## Slide 6: Inaccuracies in Floating Point Addition
Floating point addition has inherent rounding error
  Shift, round, cancellation
F.p. addition is not associative
  For the accumulator, the total error is data dependent
We’ve seen as many as 50% of mantissa bits being in error after accumulating large synthetic data sets
In general, to improve accuracy:
  multiple passes over dataset (sorting),
  multiple operations per input (additional dependencies), or
  increased precision (lower clock rate, higher latency)
…each reduces throughput
ReConFig 2013 Ph.D. Forum 6

## Slide 7: Compensated Summation
  Error Free Transformation
  a + b = x + e, x = fl(a  b)
Compensated summation
  Preserve the rounding error from each addition
  Incorporate the errors into the final result
Three strategies:
  Incorporate rounding errors from previous addition into subsequent addition
  Accumulate the error separately and incorporate total error into the final result
  Use extended precision adder (80- and 128-bit)

## Slide 8: Error Extraction
Relies on custom floating point adder that produces the roundoff error as a second output
Design | Slices | Latency | %Change Slices
64-bit FP adder | 1130 | 14 | 
64-bit “error producing“ adder | 2310 | 14 | +104.4%
80-bit FP adder | 1715 | 19 | +51.7%
128-bit FP adder | 3327 | 26 | +194.4%
ReConFig 2013 Ph.D. Forum 8

## Slide 9: Adaptive Error Compensation in Subsequent Addition (AECSA)
ReConFig 2013 Ph.D. Forum 9

## Slide 10: Accumulated Error Compensation
a
b
Sum
Value Reduction Circuit (VRC)
Custom Adder
Input FIFO
Select
FP Adder
Error FIFO
FP Adder
Select
Input Error
e1
e2
Error
Final Result
Error Reduction Circuit (ERC)
Accumulate the extracted error, compensate in the end
Error Set Status
ReConFig 2013 Ph.D. Forum 10

## Slide 11: Preview of Results
Varying к and Exp. Range = 32, Set Size = 100
ReConFig 2013 Ph.D. Forum 11
Exp. Range | к | Red. Ckt. | AECSA | AEC | EPRC80 | EPRC128
32 | 10.0 | 1.6 | 0 | 0 | 0 | 0
32 | 95.0 | 3.5 | 0.3 | 0.3 | 0.2 | 0.2
32 | 800.0 | 4.2 | 0.7 | 0.6 | 0.3 | 0.3
32 | 1600.0 | 7.7 | 0.9 | 0.7 | 0.4 | 0.4
32 | 6000.0 | 7.9 | 1.4 | 1.1 | 1.1 | 0.9
32 | 11000.0 | 8.3 | 2.5 | 1.6 | 1.4 | 1.4
Number of LSBs in Mantissa in Error
(Compared with infinite precision)