## Slide 1: Lecture 1 Introduction to Computer Architecture
Topics
  Representations of Data
  Computer Architecture
  C Programming
  Unsigned Integers
  Signed magnitude
  Two’s complement
January 16, 2018
CSCE 212H Computer Architecture

## Slide 2: Course Pragmatics
Syllabus
  Instructor: Manton Matthews
  Website: http://www.cse.sc.edu/~matthews/Courses/212/index.html
  Text
    "Computer Systems: A Programmer's Perspective" 3rd edition by Randal E. Bryant and David O'Hallaron, Prentice-Hall 2016.
  Important Dates on website
  Academic Integrity
  Slides are based on text, some directly supplied by the authors

## Slide 3: What is Computer Architecture?
Computer Architecture is the attributes of a [computing] system as seen by the programmer, i.e. the conceptual structure and functional behavior, as distinct from the organization of the data flows and controls the logic design, and the physical implementation. – Amdahl, Blaaw, and Brooks, 1964
The term computer architecture was first used in 1964 the designers of the IBM System/360.
The IBM/360 was a family of computers all with the same architecture, but with a variety of organizations(implementations).

## Slide 4: What and Why for this course
Architecture from the programmer perspective
  Use knowledge of architecture to improve performance
Topics
  Representations of Data
  Basic Computer Organization
  Instruction Set Design
  Pipelining
  HDL
  Memory Hierarchies
  Basics of Performance Evaluation
  Interconnection Basics
The goal is to provide foundational knowledge in the structure and organization of machines to enable you to write better programs

## Slide 5: Umax, Tmax, Tmin, Max Float
Unsigned
Two’s complement
Floats
Doubles

## Slide 6: Great Reality #1: Ints are not Integers, Floats are not Reals
Carnegie Mellon
Example 1: Is x2 ≥ 0?
  Float’s: Yes!
  Int’s:
    40000 * 40000 ➙ 1,600,000,000
    50000 * 50000 ➙ ??
Example 2: Is (x + y) + z = x + (y + z)?
  Unsigned & Signed Int’s: Yes!
  Float’s:
    (1e20 + -1e20) + 3.14 --> 3.14
    1e20 + (-1e20 + 3.14) --> ??
Source: xkcd.com/571

## Slide 7: Computer Arithmetic
Carnegie Mellon
Does not generate random values
  Arithmetic operations have important mathematical properties
Cannot assume all “usual” mathematical properties
  Due to finiteness of representations
  Integer operations satisfy “ring” properties
    Commutativity, associativity, distributivity
  Floating point operations satisfy “ordering” properties
    Monotonicity, values of signs
Observation
  Need to understand which abstractions apply in which contexts
  Important issues for compiler writers and serious application programmers

## Slide 8: Great Reality #2: You’ve Got to Know Assembly
Carnegie Mellon
Chances are, you’ll never write programs in assembly
  Compilers are much better & more patient than you are
But: Understanding assembly is key to machine-level execution model
  Behavior of programs in presence of bugs
    High-level language models break down
  Tuning program performance
    Understand optimizations done / not done by the compiler
    Understanding sources of program inefficiency
  Implementing system software
    Compiler has machine code as target
    Operating systems must manage process state
  Creating / fighting malware
    x86 assembly is the language of choice!

## Slide 9: Great Reality #3: Memory Matters Random Access Memory Is an Unphysical Abstraction
Carnegie Mellon
Memory is not unbounded
  It must be allocated and managed
  Many applications are memory dominated
Memory referencing bugs especially pernicious
  Effects are distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 10: Memory Referencing Bug Example
Carnegie Mellon
  Result is system specific
fun(0) ➙ 3.14
fun(1) ➙ 3.14
fun(2) ➙ 3.1399998664856
fun(3) ➙ 2.00000061035156
fun(4) ➙ 3.14
fun(6) ➙ Segmentation fault
typedef struct {
int a[2];
double d;
} struct_t;
double fun(int i) {
volatile struct_t s;
s.d = 3.14;
s.a[i] = 1073741824; /* Possibly out of bounds */
return s.d;
}

## Slide 11: Memory Referencing Bug Example
Carnegie Mellon
typedef struct {
int a[2];
double d;
} struct_t;
fun(0) ➙ 3.14
fun(1) ➙ 3.14
fun(2) ➙ 3.1399998664856
fun(3) ➙ 2.00000061035156
fun(4) ➙ 3.14
fun(6) ➙ Segmentation fault
Location accessed by fun(i)
Explanation:
Critical State | 6
? | 5
? | 4
d7 ... d4 | 3
d3 ... d0 | 2
a[1] | 1
a[0] | 0
struct_t

## Slide 12: Memory Referencing Errors
Carnegie Mellon
C and C++ do not provide any memory protection
  Out of bounds array references
  Invalid pointer values
  Abuses of malloc/free
Can lead to nasty bugs
  Whether or not bug has any effect depends on system and compiler
  Action at a distance
    Corrupted object logically unrelated to one being accessed
    Effect of bug may be first observed long after it is generated
How can I deal with this?
  Program in Java, Ruby, Python, ML, …
  Understand what possible interactions may occur
  Use or develop tools to detect referencing errors (e.g. Valgrind)

## Slide 13: Great Reality #4: There’s more to performance than asymptotic complexity
Carnegie Mellon
Constant factors matter too!
And even exact op count does not predict performance
  Easily see 10:1 performance range depending on how code written
  Must optimize at multiple levels: algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs compiled and executed
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 14: Memory System Performance Example
Carnegie Mellon
Hierarchical memory organization
Performance depends on access patterns
  Including how step through multi-dimensional array
void copyji(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (j = 0; j < 2048; j++)
for (i = 0; i < 2048; i++)
dst[i][j] = src[i][j];
}
void copyij(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (i = 0; i < 2048; i++)
for (j = 0; j < 2048; j++)
dst[i][j] = src[i][j];
}
81.8ms
4.3ms
2.0 GHz Intel Core i7 Haswell

## Slide 15: Why The Performance Differs
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
copyij
copyji

## Slide 16: Great Reality #5: Computers do more than execute programs
Carnegie Mellon
They need to get data in and out
  I/O system critical to program reliability and performance
They communicate with each other over networks
  Many system-level issues arise in presence of network
    Concurrent operations by autonomous processes
    Coping with unreliable media
    Cross platform compatibility
    Complex performance issues

## Slide 17: Bits and Bytes
  Why bits?
  Representing information as bits
    Binary/Hexadecimal
    Byte representations
      numbers
      characters and strings
      Instructions
  Bit-level manipulations
    Boolean algebra
    Expressing in C
How much C do we Know?

## Slide 18: Byte-Oriented Memory Organization
Programs Refer to Virtual Addresses
  Conceptually very large array of bytes
  Actually implemented with hierarchy of different memory types
    SRAM, DRAM, disk
    Only allocate for regions actually used by program
  In Unix and Windows NT, address space private to particular “process”
    Program being executed
    Program can clobber its own data, but not that of others
Compiler + Run-Time System Control Allocation
  Where different program objects should be stored
  Multiple mechanisms: static, stack, and heap
  In any case, all allocation within single virtual address space

## Slide 19: Words
Machine Has “Word Size”
  Nominal size of integer-valued data
    Including addresses
  Most current machines are 32 bits (4 bytes)
    Limits addresses to 4GB
    Becoming too small for memory-intensive applications
  High-end systems are 64 bits (8 bytes)
    Potentially address  1.8 X 1019 bytes
  Machines support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes
Word-Oriented Memory Organization

## Slide 20: Byte Order
Big Endian
  Least significant byte has highest address
Little Endian
  Least significant byte has lowest address
Example
  Variable x has 4-byte representation 0x01234567
  Address given by &x is 0x100

## Slide 21: Reading Byte-Reversed Listings
Disassembly
  Text representation of binary machine code
  Generated by program that reads machine code
Example Fragment
Address Instruction Code Assembly Rendition
8048365: 5b pop %ebx
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
804836c: 83 bb 28 00 00 00 00 cmpl $0x0,0x28(%ebx)
Deciphering Numbers
  Value: 0x12ab
  Pad to 4 bytes: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse: ab 12 00 00

## Slide 22: Code to Print Byte Representation of Data
typedef unsigned char *pointer;
void show_bytes(pointer start, int len)
{
int i;
for (i = 0; i < len; i++)
printf("0x%p\t0x%.2x\n",
start+i, start[i]);
printf("\n");
}
Printf directives:
  %p: Print pointer
  %x: Print Hexadecimal

## Slide 23: show_bytes Execution Example
int a = 15213;
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux):
int a = 15213;
0x11ffffcb8 0x6d
0x11ffffcb9 0x3b
0x11ffffcba 0x00
0x11ffffcbb 0x00

## Slide 24: Strings
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Other encodings exist, but uncommon
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
    Data are single byte quantities
  Text files generally platform independent
    Except for different conventions of line termination character(s)!

## Slide 25: Machine-Level Code Representation
Encode Program as Sequence of Instructions
  Each simple operation
    Arithmetic operation
    Read or write memory
    Conditional branch
  Instructions encoded as bytes
    Alpha’s, Sun’s, Mac’s use 4 byte instructions
      Reduced Instruction Set Computer (RISC)
    PC’s use variable length instructions
      Complex Instruction Set Computer (CISC)
  Different instruction types and encodings for different machines
    Most code not binary compatible
Programs are Byte Sequences Too!

## Slide 26: Relations Between Operations
DeMorgan’s Laws
  Express & in terms of |, and vice-versa
    A & B = ~(~A | ~B)
      A and B are true if and only if neither A nor B is false
    A | B = ~(~A & ~B)
      A or B are true if and only if A and B are not both false
Exclusive-Or using Inclusive Or
    A ^ B = (~A & B) | (A & ~B)
      Exactly one of A and B is true
    A ^ B = (A | B) & ~(A & B)
      Either A is true, or B is true, but not both

## Slide 27: General Boolean Algebras
Operate on Bit Vectors
  Operations are applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 28: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j  A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 29: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 --> 0xBE
    ~010000012 --> 101111102
  ~0x00 --> 0xFF
    ~000000002 --> 111111112
  0x69 & 0x55 --> 0x41
    011010012 & 010101012 --> 010000012
  0x69 | 0x55 --> 0x7D
    011010012 | 010101012 --> 011111012

## Slide 30: Contrast: Logic Operations in C
Contrast to Logical Operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 --> 0x00
  !0x00 --> 0x01
  !!0x41 --> 0x01
  0x69 && 0x55 --> 0x01
  0x69 || 0x55 --> 0x01
  p && *p (avoids null pointer access)

## Slide 31: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
    Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on right
    Useful with two’s complement integer representation

## Slide 32: XOR
  Bitwise Xor is form of addition
  With extra property that every value is its own additive inverse
    A ^ A = 0
void funny(int *x, int *y)
{
*x = *x ^ *y; /* #1 */
*y = *x ^ *y; /* #2 */
*x = *x ^ *y; /* #3 */
}

## Slide 33: Encoding Integers
short int x = 15213;
short int y = -15213;
  C short 2 bytes long
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Two’s Complement
Sign
Bit

## Slide 34: Encoding Example (Cont.)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 35: Numeric Ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 36: Values for Different Word Sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
    K&R App. B11
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform-specific

## Slide 37: Casting Signed to Unsigned
short int x = 15213;
unsigned short int ux = (unsigned short) x;
short int y = -15213;
unsigned short int uy = (unsigned short) y;
C Allows Conversions from Signed to Unsigned
Resulting Value
  No change in bit representation
  Nonnegative values unchanged
    ux = 15213
  Negative values change into (large) positive values
    uy = 50323

## Slide 38: Relation Between Signed & Unsigned
  uy = y + 2 * 32768 = y + 65536

## Slide 39: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;

## Slide 40: Casting Surprises
  0 0U == unsigned
  -1 0 < signed
  -1 0U > unsigned
  2147483647 -2147483648 > signed
  2147483647U -2147483648 < unsigned
  -1 -2 > signed
  (unsigned) -1 -2 > unsigned
  2147483647 2147483648U < unsigned
  2147483647 (int) 2147483648U > signed
Expression Evaluation
  If mix unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32
Constant1 Constant2 Relation Evaluation
  0 0U
  -1 0
  -1 0U
  2147483647 -2147483648
  2147483647U -2147483648
  -1 -2
  (unsigned) -1 -2
  2147483647 2147483648U
  2147483647 (int) 2147483648U

## Slide 41: Explanation of Casting Surprises
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Comp.
Range
Unsigned
Range
2’s Comp.  Unsigned
  Ordering Inversion
  Negative  Big Positive

## Slide 42: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 43: Sign Extension Example
  Converting from smaller to larger integer data type
  C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 44: Justification For Sign Extension
Prove Correctness by Induction on k
  Induction Step: extending by single bit maintains value
  Key observation: –2w–1 = –2w +2w–1
  Look at weight of upper bits:
    X –2w–1 xw–1
    X  –2w xw–1 + 2w–1 xw–1 = –2w–1 xw–1
-
• • •
X
X 
-
+
• • •
w+1
w

## Slide 45: Why Should I Use Unsigned?
Don’t Use Just Because Number Nonzero
  C compilers on some machines generate less efficient code
    unsigned i;
    for (i = 1; i < cnt; i++)
    a[i] += a[i-1];
  Easy to make mistakes
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
Do Use When Performing Modular Arithmetic
  Multiprecision arithmetic
  Other esoteric stuff
Do Use When Need Extra Bit’s Worth of Range
  Working right up to limit of word size

## Slide 46: Negating with Complement & Increment
Claim: Following Holds for 2’s Complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…112 == -1
Increment
  ~x + x + (-x + 1) == -1 + (-x + 1)
  ~x + 1 == -x
Warning: Be cautious treating int’s as integers
  OK here
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1

## Slide 47: Comp. & Incr. Examples
x = 15213
0

## Slide 48: Unsigned Addition
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)

## Slide 49: Mathematical Properties
Modular Addition Forms an Abelian Group
  Closed under addition
    0  UAddw(u , v)  2w –1
  Commutative
    UAddw(u , v) = UAddw(v , u)
  Associative
    UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  0 is additive identity
    UAddw(u , 0) = u
  Every element has additive inverse
    Let UCompw (u ) = 2w – u
    UAddw(u , UCompw (u )) = 0

## Slide 50: Two’s Complement Addition
TAdd and UAdd have Identical Bit-Level Behavior
  Signed vs. unsigned addition in C:
  int s, t, u, v;
  s = (int) ((unsigned) u + (unsigned) v);
  t = u + v
  Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)

## Slide 51: Characterizing TAdd
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
–2w –1
–2w
0
2w –1
2w–1
True Sum
TAdd Result
1 000…0
1 100…0
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
PosOver
NegOver
(NegOver)
(PosOver)
u
v
< 0
> 0
< 0
> 0
NegOver
PosOver
TAdd(u , v)

## Slide 52: Detecting 2’s Comp. Overflow
Task
  Given s = TAddw(u , v)
  Determine if s = Addw(u , v)
  Example
  int s, u, v;
  s = u + v;
Claim
  Overflow iff either:
    u, v < 0, s  0 (NegOver)
    u, v  0, s < 0 (PosOver)
  ovf = (u<0 == v<0) && (u<0 != s<0);
0
2w –1
2w–1
PosOver
NegOver

## Slide 53: Mathematical Properties of TAdd
Isomorphic Algebra to UAdd
  TAddw(u , v) = U2T(UAddw(T2U(u ), T2U(v)))
    Since both have identical bit patterns
Two’s Complement Under TAdd Forms a Group
  Closed, Commutative, Associative, 0 is additive identity
  Every element has additive inverse
    Let TCompw (u ) = U2T(UCompw(T2U(u ))
    TAddw(u , TCompw (u )) = 0

## Slide 54: Unsigned vs. Signed Multiplication
Unsigned Multiplication
  unsigned ux = (unsigned) x;
  unsigned uy = (unsigned) y;
  unsigned up = ux * uy
  Truncates product to w-bit number up = UMultw(ux, uy)
  Modular arithmetic: up = ux  uy mod 2w
Two’s Complement Multiplication
  int x, y;
  int p = x * y;
  Compute exact product of two w-bit numbers x, y
  Truncate result to w-bit number p = TMultw(x, y)

## Slide 55: Unsigned vs. Signed Multiplication
Unsigned Multiplication
  unsigned ux = (unsigned) x;
  unsigned uy = (unsigned) y;
  unsigned up = ux * uy
Two’s Complement Multiplication
  int x, y;
  int p = x * y;
Relation
  Signed multiplication gives same bit-level result as unsigned
  up == (unsigned) p

## Slide 56: Properties of Two’s Comp. Arithmetic
Isomorphic Algebras
  Unsigned multiplication and addition
    Truncating to w bits
  Two’s complement multiplication and addition
    Truncating to w bits
Both Form Rings
  Isomorphic to ring of integers mod 2w
Comparison to Integer Arithmetic
  Both are rings
  Integers obey ordering properties, e.g.,
    u > 0  u + v > v
    u > 0, v > 0  u · v > 0
  These properties are not obeyed by two’s comp. arithmetic
    TMax + 1 == TMin
    15213 * 30426 == -10030 (16-bit words)

## Slide 57: C Puzzles
  Taken from old exams
  Assume machine with 32 bit word size, two’s complement integers
  For each of the following C expressions, either:
    Argue that is true for all argument values
    Give example where not true
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0
int x = foo();
int y = bar();
unsigned ux = x;
unsigned uy = y;
Initialization

## Slide 58: C Puzzle Answers
  Assume machine with 32 bit word size, two’s comp. integers
  TMin makes a good counterexample in many cases
x < 0  ((x*2) < 0) False: TMin
ux >= 0 True: 0 = UMin
x & 7 == 7  (x<<30) < 0 True: x1 = 1
ux > -1 False: 0
x > y  -x < -y False: -1, TMin
x * x >= 0 False: 30426
x > 0 && y > 0  x + y > 0 False: TMax, TMax
x >= 0  -x <= 0 True: –TMax < 0
x <= 0  -x >= 0 False: TMin
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0