## Slide 1: Lecture 10 Logic Design Review & HCL & Bomb Lab
Topics
  211 review
    Comparators
    Multiplexors
    decoders
  Hardware Control Language (HCL)
February 20, 2018
CSCE 212 Computer Architecture

## Slide 2: Today
Bomblab
Bombserver matthewsCM = 129.252.11.236:15213
Logic design review
Hardware Description languages
  Like a program except specifies hardware component
  Verilog
  VHDL
  CSAPP version -- Hardware Control Language (HCL)

## Slide 3: Aggregate data - Arrays
double a[53][62];
…
sum = 0.0
for i
for j
sum = sum + a[i][j]
Today is Pi –day
Finding pi in unix
locate pi
/usr/include/math.h

## Slide 4: Structures and Unions; Arrays of Structures
struct student{
int id;
double gpa;
char * name;
struct student *link;
}
union unode{
int id;
…
struct student *link;
}
struct student roll[57];
struct student r145[14][24];

## Slide 5: Combinational Circuits
Acyclic Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Acyclic Network
Primary
Inputs
Primary
Outputs

## Slide 6: Bit Equality
  Generate 1 if a and b are equal
Hardware Control Language (HCL)
  Very simple hardware description language
    Boolean operations have syntax similar to C logical operations
  We’ll use it to describe control logic for processors
Bit equal
a
b
eq
bool eq = (a&&b)||(!a&&!b)
HCL Expression

## Slide 7: Word Equality
  64-bit word size
  HCL representation
    Equality operation
    Generates Boolean value
b63
Bit equal
a63
eq63
b62
Bit equal
a62
eq62
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
Eq
=
B
A
Eq
Word-Level Representation
bool Eq = (A == B)
HCL Representation

## Slide 8: Decoders – n x 2n decoder

## Slide 9: Bit-Level Multiplexor
  Control signal s
  Data signals a and b
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out
bool out = (s&&a)||(!s&&b)
HCL Expression

## Slide 10: Word Multiplexor
  Select input word A or B depending on control signal s
  HCL representation
    Case expression
    Series of test : value pairs
    Output value for first successful test
Word-Level Representation
HCL Representation
b63
s
a63
out63
b62
a62
out62
b0
a0
out0
int Out = [
s : A;
1 : B;
];
s
B
A
Out
MUX

## Slide 11: HCL Word-Level Examples
  Find minimum of three input words
  HCL case expression
  Final case guarantees match
A
Min3
MIN3
B
C
int Min3 = [
A < B && A < C : A;
B < A && B < C : B;
1 : C;
];
D0
D3
Out4
s0
s1
MUX4
D2
D1
  Select one of 4 inputs based on two control bits
  HCL case expression
  Simplify tests by assuming sequential matching
int Out4 = [
!s1&&!s0: D0;
!s1 : D1;
!s0 : D2;
1 : D3;
];
Minimum of 3 Words
4-Way Multiplexor

## Slide 12: Arithmetic Logic Unit
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Combinational logic
    Continuously responding to inputs
  Control signal selects function computed
    Corresponding to 4 arithmetic/logical operations in Y86-64
  Also computes values for condition codes
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B

## Slide 13: Storing and Accessing 1 Bit
Q+
Q–
R
S
R-S Latch
Resetting
1
0
1
0
0
1
Setting
0
1
0
1
1
0
Storing
0
0
!q
q
q
!q
Bistable Element
Q+
Q–
q
!q
q = 0 or 1

## Slide 14: 1-Bit Latch
D Latch
Q+
Q–
R
S
D
C
Data
Clock
Latching
1
d
!d
!d
!d
d
d
d
!d
0
Storing
d
!d
q
!q
!q
q
0
0

## Slide 15: Transparent 1-Bit Latch
  When in latching mode, combinational propogation from D to Q+ and Q–
  Value latched depends on value of D as C falls
C
D
Q+
Time
Changing D
Latching
1
d
!d
!d
!d
d
d
d
!d

## Slide 16: Edge-Triggered Latch
  Only in latching mode for brief period
    Rising clock edge
  Value latched depends on data as clock rises
  Output remains stable at all other times
Q+
Q–
R
S
D
C
Data
Clock
T
Trigger
C
D
Q+
Time
T

## Slide 17: Registers
  Stores word of data
    Different from program registers seen in assembly code
  Collection of edge-triggered latches
  Loads input on rising edge of clock
I
O
Clock
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
i7
i6
i5
i4
i3
i2
i1
i0
o7
o6
o5
o4
o3
o2
o1
o0
Clock
Structure

## Slide 18: Register Operation
  Stores data bits
  For most of time acts as barrier between input and output
  As clock rises, loads input
State = x
Rising
clock

Output = x
Input = y
x

State = y
Output = y
y

## Slide 19: State Machine Example
  Accumulator circuit
  Load or accumulate on each cycle
Comb. Logic
A
L
U
0
Out
MUX
0
1
Clock
In
Load
x0
x1
x2
x3
x4
x5
x0
x0+x1
x0+x1+x2
x3
x3+x4
x3+x4+x5
Clock
Load
In
Out

## Slide 20: Random-Access Memory
  Stores multiple words of memory
    Address input specifies which word to read or write
  Register file
    Holds values of program registers
    %rax, %rsp, etc.
    Register identifier serves as address
      ID 15 (0xF) implies no read or write performed
  Multiple Ports
    Can read and/or write multiple words in one cycle
      Each has separate address and data input/output
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 21: Register File Timing
Reading
  Like combinational logic
  Output data generated based on input address
    After some delay
Writing
  Like register
  Update only as clock rises
Register
file
A
B
srcA
valA
srcB
valB
y
2
Register
file
W
dstW
valW
Clock
x
2
Rising
clock


Register
file
W
dstW
valW
Clock
y
2
x
2
x
2

## Slide 22: Hardware Control Language
  Very simple hardware description language
  Can only express limited aspects of hardware operation
    Parts we want to explore and modify
Data Types
  bool: Boolean
    a, b, c, …
  int: words
    A, B, C, …
    Does not specify word size---bytes, 64-bit words, …
Statements
  bool a = bool-expr ;
  int A = int-expr ;

## Slide 23: HCL Operations
  Classify by type of value returned
Boolean Expressions
  Logic Operations
    a && b, a || b, !a
  Word Comparisons
    A == B, A != B, A < B, A <= B, A >= B, A > B
  Set Membership
    A in { B, C, D }
      Same as A == B || A == C || A == D
Word Expressions
  Case expressions
    [ a : A; b : B; c : C ]
    Evaluate test expressions a, b, c, … in sequence
    Return word expression A, B, C, … for first successful test

## Slide 24: Summary
Computation
  Performed by combinational logic
  Computes Boolean functions
  Continuously reacts to input changes
Storage
  Registers
    Hold single words
    Loaded as clock rises
  Random-access memories
    Hold multiple words
    Possible multiple read or write ports
    Read word when address input changes
    Write word as clock rises