## Slide 1: Lecture 16 The Memory Hierarchy
Topics
  Exceptions and Pipelines
  Review of a few things
  Memory Hierarchy
April 9, 2018
CSCE 212 Computer Architecture

## Slide 2: Register Calling Again
Carnegie Mellon
Registers
First 6 arguments
Return value
Stack
Only allocate stack space when needed
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
Arg 7
• • •
Arg 8
Arg n
• • •

## Slide 3: x86-64 Linux Register Usage #1
Carnegie Mellon
%rax
  Return value
  Also caller-saved
  Can be modified by procedure
%rdi, ..., %r9
  Arguments
  Also caller-saved
  Can be modified by procedure
%r10, %r11
  Caller-saved
  Can be modified by procedure
%rax
%rdx
%rcx
Return value
%r8
%r9
%r10
%r11
%rdi
%rsi
Arguments
Caller-saved
temporaries

## Slide 4: x86-64 Linux Register Usage #2
Carnegie Mellon
%rbx, %r12, %r13, %r14
  Callee-saved
  Callee must save & restore
%rbp
  Callee-saved
  Callee must save & restore
  May be used as frame pointer
  Can mix & match
%rsp
  Special form of callee save
  Restored to original value upon exit from procedure
%rbx
%rsp
Callee-saved
Temporaries
Special
%rbp
%r12
%r13
%r14

## Slide 5: Callee-Saved Example #1
Carnegie Mellon
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Initial Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx

## Slide 6: Callee-Saved Example #2
Carnegie Mellon
call_incr2:
pushq %rbx
subq $16, %rsp
movq %rdi, %rbx
movq $15213, 8(%rsp)
movl $3000, %esi
leaq 8(%rsp), %rdi
call incr
addq %rbx, %rax
addq $16, %rsp
popq %rbx
ret
long call_incr2(long x) {
long v1 = 15213;
long v2 = incr(&v1, 3000);
return x+v2;
}
%rsp
Pre-return Stack Structure
. . .
Rtn address
15213
Unused
%rsp
Resulting Stack Structure
. . .
Rtn address
%rsp+8
Saved %rbx

## Slide 7: ManyArg.c Homework assignment
Functions that have a variable number of arguments?
Can you recall an example?
Hint stdio.
How is this possible?
Can you write your own functions with a variable number of arguments?
  Yes
  stdarg (3) - variable argument lists
  va_arg (3) - variable argument lists

## Slide 8: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
RAM comes in two varieties:
  SRAM (Static RAM)
  DRAM (Dynamic RAM)

## Slide 9: SRAM vs DRAM Summary
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 4 or 6 1X No Maybe 100x Cache memories
DRAM 1 10X Yes Yes 1X Main memories,
frame buffers

## Slide 10: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs. with partial (block-level) erase capability
    Wears out after about 100,000 erasings
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 11: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 12: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor
and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 13: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 14: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
  Typical Tavg rotation = 7200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 15: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 16: Solid State Disks (SSDs)
Pages: 512KB to 4KB, Blocks: 32 to 128 pages
Data read/written in units of pages.
Page can be written only after its block has been erased
A block wears out after about 100,000 repeated writes.
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks

## Slide 17: SSD Performance Characteristics
Sequential access faster than random access
  Common theme in the memory hierarchy
Random writes are somewhat slower
  Erasing a block takes a long time (~1 ms)
  Modifying a block page requires all other pages to be copied to new block
  In earlier SSDs, the read/write gap was much larger.
Sequential read tput 550 MB/s Sequential write tput 470 MB/s
Random read tput 365 MB/s Random write tput 303 MB/s
Avg seq read time 50 us Avg seq write time 60 us
Source: Intel SSD 730 product specification.

## Slide 18: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    E.g. Intel SSD 730 guarantees 128 petabyte (128 x 1015 bytes) of writes before they wear out
  In 2015, about 30 times more expensive per byte
Applications
  MP3 players, smart phones, laptops
  Beginning to appear in desktops and servers

## Slide 19: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk

## Slide 20: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 21: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 22: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 23: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 24: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}

## Slide 25: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 26: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 27: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea: The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 28: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 29: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 30: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 31: General Caching Concepts: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 32: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 33: Average Memory Access Time