## Slide 1: Lecture 3 Instruction Level Parallelism (Pipelining)
Topics
  Execution time
  ILP
Readings: Appendix C
September 6, 2017
CSCE 513 Computer Architecture

## Slide 2: Overview
Last Time
  Overview:
  Speed-up
  Power wall, ILP wall,  to multicore
  Def Computer Architecture
  Lecture 1 slides 1-29?
New
  Syllabus and other course pragmatics
    Website (not shown)
    Dates
  Figure 1.9 Trends: CPUs, Memory, Network, Disk
  Why geometric mean?
  Speed-up again
  Amdahl’s Law

## Slide 3: Finish up Slides from Lecture 2
Slides 18 
CPU Performance Equation
Fallacies and Pitfalls
List of Appendices

## Slide 4: Patterson’s 5 steps to design a processor
Analyze instruction set => datapath requirements
Select set of data-path components & establish clock methodology
Assemble data-path meeting the requirements
Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
Assemble the control logic

## Slide 5: Components we are assuming you know
Basic Gates
  Ands, ors, xors, nands, nors
Combinational components
  Adders
  ALU
  Multiplexers (MUXs)
  Decoders
  Not going to need: PLAs, PALs, FPGAs …
Sequential Components
  Registers
  Register file: banks of registers, pair of Mux, decoder for load lines
  Memories
Register Transfer Language
  NonBranch: PC  PC + 4 (control signal: register transfer)

## Slide 6: MIPS Simplifies Processor Design
Instructions same size
Source registers always in same place
Immediates are always same size, same location
Operations always on registers or immediates
Single cycle data path means …
CPI is …
CCT is …
Reference http://en.wikipedia.org/wiki/MIPS_architecture
Ref: http://en.wikipedia.org/wiki/MIPS_architecture

## Slide 7: Register File
32:1 Mux
32:1 Mux
R0
R31
5x32
decoder
Rd
Rt
Rs
Data in
Bus A
Bus B
Notes
How big are the lines ?
  Some 5
  Some 32
  Some 1
Data-In goes to every register
R0 = 0

## Slide 8: Instruction Fetch (non-branch)

## Slide 9: High Level for Register-Register Instruct.

## Slide 10: Stores: Store Rs, disp(Rb)
Notes
    Sign extend for 16bit immediates
    Write trace
    Read trace

## Slide 11: Loads LD rd, disp(Rr)
Notes
  Sign extend for 16bit (disp) to calculate address = disp + Rr

## Slide 12: Branches
Notes
  Sign extend for backwards branches
  Note Shift left 2 = Multiply by 4  which means displacement is in words
  Register Transfer Language
  Cond R[rs] == R[rt]
  if (COND eq 0)
    PC  PC + 4 + (SE(imm16) x 4 )
  else
    PC  PC + 4

## Slide 13: Branch Hardware
imm16
PC
Clk
Adder
Mux
Adder
4
nPC_sel
PC Ext
Inst Address

## Slide 14: Adding Instruction Fetch / PC Increment

## Slide 15: Simple Data Path for All Instructions

## Slide 16: Pulling it All Together
Notes
  Note PC=PC+4 (all MIPS instructions are 4 bytes)

## Slide 17: Adding Control

## Slide 18: Non-pipelined RISC operations Fig C.21
Store 4 cycles (10%) CPI ?
Branches 2 cycles (12%)
Others 5 cycles (78%)

## Slide 19: Multicycle Data Path (appendix C)
Multicycle Data Path
  Execute instructions in stages
  Shorter Clock Cycle Time (CCT)
  Executing an instruction takes a few cycles
    (how many stages we have)
  We can execute different things in each stage at the same time; precursor to the pipelined version
Stages
  Fetch
  Decode
  Execute
  Memory
  Write Back

## Slide 20: Stages of Classical 5-stage pipeline
Instruction Fetch Cycle
  IR  Mem[PC]
  NPC  PC + 4
Decode
  A  Regs[rs]
  B 
  Imm  sign-extend of
Execute
  .
Memory
  .
Write Back
  .

## Slide 21: Execute
Based on type of intsruction
Memory Reference – calculate effective address d(rb)
  ALUOutput  A + Imm
Register-Register ALU instruction
  ALUOutput  A func B
Register-Immediate ALU instruction
  ALUOutput  A op Imm
Branch
  ALUOutput  NPC + (Imm <<2)
  Cond  (A==0)

## Slide 22: Memory
  PC  NPC
Memory
  LMD  Mem[ALUOutput], or
  Mem[ALUOutput]  B
Branch
  If (cond) PC  ALUOutput

## Slide 23: Write-back (WB) cycle
Register-Register ALU instruction
  Regs[rd]  ALUOutput
Register-Immediate ALU instruction
  Regs[rt]  ALUOutput
Load Instruction
  Regs[rt]  LMD

## Slide 24: Simple RISC Pipeline
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  | IF | ID | EX | MEM | WB
Instruction
Instruction n
Instruction n+1
Instruction n+2
Instruction n+3
Instruction n+4
Clock cycle number (time )

## Slide 25: Performance Analysis in Perfect World
Assuming S stages in the pipeline.
At each cycle a new instruction is initiated.
To execute N instructions takes:
N cycles to start-up instructions
(S-1) cycles to flush the pipeline
TotalTime = N + (S-1)
Example for S=5 from previous slide N=100 instructions
Time to execute in non-pipelined = 100 * 5 = 500 cycles
Time to execute in pipelined version = 100 + (5-1) = 104 cycles
SpeedUp = …

## Slide 26: Implement Pipelines Supp. Fig C.4

## Slide 27: Pipeline Example with a problem (A.5 like)
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
IM | ID | EX | DM | WB |  |  |  | 
 | IM | ID | EX | DM | WB |  |  | 
 |  | IM | ID | EX | DM | WB |  | 
 |  |  | IM | ID | EX | DM | WB | 
 |  |  |  | IM | ID | EX | DM | WB
DADD
DSUB
AND
OR
XOR
Instruction
R1, R2, R3
R4, R1, R5
R6, R1, R7
R8, R1, R9
R10, R1, R11

## Slide 28: Inserting Pipeline Registers into Data Path fig A’.18

## Slide 29: Major Hurdle of Pipelining
Consider executing the code below
DADD R1, R2, R3 /* R1 R2 + R3 */
DSUB R4, R1, R5 /* R4 R1 + R5 */
AND R6, R1, R7 /* R6 R1 + R7 */
OR R8, R1, R9 /* R8 R1 | R9 */
XOR R10, R1, R11 /* R10  R1 ^ R11 */

## Slide 30: RISC Pipeline Problems
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
IM | ID | EX | DM | WB |  |  |  | 
 | IM | ID | EX | DM | WB |  |  | 
 |  | IM | ID | EX | DM | WB |  | 
 |  |  | IM | ID | EX | DM | WB | 
 |  |  |  | IM | ID | EX | DM | WB
DADD
DSUB
AND
OR
XOR
Clock cycle number (time )
Instruction
R1, R2, R3
R4, R1, R5
R6, R1, R7
R8, R1, R9
R10, R1, R11
So what’s the problem?

## Slide 31: Hazards
Data Hazards – a data value computed in one stage is not ready when it is needed in another stage of the pipeline
Simple Solution: stall until it is ready but we can do better
Control or Branch Hazards
Structural Hazards – arise when resources are not sufficient to completely overlap instruction sequence e.g. two floating point add units then having to do three simultaneously

## Slide 32: Performance of Pipelines with Stalls
Thus Pipelining can be thought of as improving CPI or improving CCT.
Relationships
Equations

## Slide 33: Performance Equations with Stalls
If we ignore overhead of pipelining
Special Case: If we assume every instruction takes same number of cycles, i.e., CPI = constant and assume this constant is the depth of the pipeline then

## Slide 34: Performance Equations with Stalls
Alternatively focusing on improvement in CCT
Then simplifying using formulas for CCTpipelined

## Slide 35: Performance Equations with Stalls
Then simplifying using formulas for CCTpipelined and
We obtain

## Slide 36: Structural Hazards
If a combination of instructions cannot be accommodated because of resource conflicts is called a structural hazard.
Examples
Single port memory (what is a dual port memory anyway?)
One write port on register file
Single floating point adder
…
A stall in pipeline frequently called a pipeline bubble or just bubble.
A bubble floats through the pipeline occupying space

## Slide 37: Example Structural Hazard Fig C.4

## Slide 38: Pipeline Stalled for Structural Hazard
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
IF | ID | EX | MEM | WB |  |  |  | 
 | IF | ID | EX | MEM* | WB |  |  | 
 |  | IF | ID | EX | MEM | WB |  | 
 |  |  | stall | IF | ID | EX | MEM | WB
 |  |  |  |  | stall | IF | ID | EX
Instruction
Instruction n
Instruction n+1
Instruction n+2
Instruction n+3
Instruction n+4
Clock cycle number (time )
MEM – a Memory cycle that is a load or Store
MEM* – a Memory cycle that is not a load or Store

## Slide 39: Data Hazards

## Slide 40: Data Hazard
1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
IM | ID | EX | DM | WB |  |  |  | 
 | IM | ID | EX | DM | WB |  |  | 
 |  | IM | ID | EX | DM | WB |  | 
 |  |  | IM | ID | EX | DM | WB | 
 |  |  |  | IM | ID | EX | DM | WB
DADD
DSUB
AND
OR
XOR
Clock cycle number (time )
Instruction
R1, R2, R3
R4, R1, R5
R6, R1, R7
R8, R1, R9
R10, R1, R11
IM – instruction Memory, DM – data memory

## Slide 41: Figure C.6

## Slide 42: Minimizing Data Hazard Stalls by Forwarding

## Slide 43: Fig C.7 Forwarding

## Slide 44: Forward of operands for Stores C.8

## Slide 45: Figure C.9 (new slide) Data Forwarding
Copyright © 2011, Elsevier Inc. All rights Reserved.
Figure C.9 The load instruction can bypass its results to the AND and OR instructions, but not to the DSUB, since that would mean forwarding the result in “negative time.”

## Slide 46: Logic to detect Hazards

## Slide 47: Figure C.23 Forwarding Paths

## Slide 48: Forwarding Figure C.26
Pipeline Reg. Source | Opcode of Source | Pipeline Reg. Destination | Opcode of Destination | Destination of forwarding | Comparison (if equal then forward )

## Slide 49
Pipeline Reg. Source | Opcode of Source | Pipeline Reg. Destination | Opcode of Destination | Destination of forwarding | Comparison (if equal then forward )

## Slide 50: Figure C.23 Forwarding Paths

## Slide 51: Load/Use Hazard

## Slide 52: Control Hazrds

## Slide 53
Figure C.18 The states in a 2-bit prediction scheme. By using 2 bits rather than 1, a branch that strongly favors taken or not taken—as many branches do—will be mispredicted less often than with a 1-bit predictor. The 2 bits are used to encode the four states in the system. The 2-bit scheme is actually a specialization of a more general scheme that has an n-bit saturating counter for each entry in the prediction buffer. With an n-bit counter, the counter can take on values between 0 and 2n – 1: When the counter is greater than or equal to one-half of its maximum value (2n – 1), the branch is predicted as taken; otherwise, it is predicted as untaken. Studies of n-bit predictors have shown that the 2-bit predictors do almost as well, thus most systems rely on 2-bit branch predictors rather than the more general n-bit predictors.

## Slide 54: Pop Quiz
Suppose that your application is 60% parallelizable what is the overall Speedup in going from 1 core to 2?
Assuming Power and Frequency are linearly related how is the Dynamic Power affected by the improvement?

## Slide 55: Plan of attack
Chapter reading plan
1
Appendix C(pipeline review)
Appendix B (Cache review)
Chapter 2 (Memory Hierarchy)
Appendix A (ISA review not really)
Chapter 3 (Instruction Level Parallelism ILP)
Chapter 4 (Data level parallelism
Chapter 5 (Thread level parallelism)
Chapter 6 (Warehouse-scale computing)
Sprinkle in other appendices
Website
Lectures
HW
Links
Errata ??
moodle
https://dropbox.cse.sc.edu/
CEC login/password
Systems
Simplescalar - pipeline
Beowulf cluster - MPI
GTX - multithreaded