## Slide 1: Lecture 4 Pipelines II
Topics
  IEEE754
  ISA and frequency counts
  Pipelining
  Data Hazards
  Forwarding
  Load-Use Hazard
  Control Hazards
Readings: Appendix C
September 13, 2017
CSCE 513 Computer Architecture

## Slide 2: Overview
Last Time
  Review of Single cycle design
  5 stage Pipeline
  Lecture 3 slides 1-20
New
  Slides 20-51 of Lecture 3
  IEEE 754 Floating Point
  Normal Pipeline Operations – the Ideal World
  Hazards
  Data Hazards: RAW, WAR, WAW, forwarding, load-use
  Control hazards
  Performance with Stalls
References
  Appendix C

## Slide 3: gcc –S matmul.c  matmul.s
matmul.c
232 lines
Inner loop
C[i][j] = 0.0;
for(x=0;x<k;++x){
C[i][j] = C[i][j] + A[i][x] * B[x][j];
}
%st - floating point on stack
%st(1) – one below it
matmul.s
690 lines
Part of Inner loop
.....
…..
movl 48(%esp), %ecx
sall $3, %ecx
addl %ecx, %eax
fldl (%eax)
fmulp %st, %st(1)
faddp %st, %st(1)
fstpl (%edx)
addl $1, 52(%esp)

## Slide 4
Figure C.2 The pipeline can be thought of as a series of data paths shifted in time. This shows the overlap among the parts of the data path, with clock cycle 5 (CC 5) showing the steady-state situation. Because the register file is used as a source in the ID stage and as a destination in the WB stage, it appears twice. We show that it is read in one part of the stage and written in another by using a solid line, on the right or left, respectively, and a dashed line on the other side. The abbreviation IM is used for instruction memory, DM for data memory, and CC for clock cycle.

## Slide 5: Appendix A – Instruction Set Architecture(ISA)
Memory Addressing
  Big Endian vs Little Endian
  alignment
Address Modes – fig A.6 (next slide)
Frequency of 80x86 Instruction Execution – fig A.7, A.13
Role of Compilers –
  Optimization
  Register allocation
MIPS review: Appendix A.9
  Registers: 32 integer reg. R0-R31(R0=0), float/double regs F0-F31

## Slide 6: Address Modes – fig A.6
Register
Immediate
Displacement
Register Indirect
Indexed
Direct
Memory Indirect
Autoincrement
scaled

## Slide 7: Frequency of Address Modes A.7
.

## Slide 8: Frequency of 80x86 Instructions A.13
.

## Slide 9: Compiler Optimizations figure A.20

## Slide 10: Figure C.22 Inserting Pipeline Registers into Data Path

## Slide 11
Fields in pipeline registers
  IF/ID.IR  ID/EX.IR  EX/MEM.IR ; Instruction copied
  ID/EX.A, ID/EX.B EX/MEM.ALUoutput …
Figure C.22 Inserting Pipeline Registers into Data Path

## Slide 12: Figure C.23

## Slide 13: Figure C.21 Examples of Data Hazards
No Dependencies with Accesses in order
Instruction |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
LD R1, 44(R2) |  |  |  |  |  |  |  |  | 
DADD R5, R6, R7 |  |  |  |  |  |  |  |  | 
DSUB R8, R6, R7 |  |  |  |  |  |  |  |  | 
OR R9, R4, R7 |  |  |  |  |  |  |  |  | 

## Slide 14: Examples of Data Hazards
Dependency requiring a stall
Note
  Instr1 = Load, … and Instr2 = DADD, DSUB, OR, AND, …
  rt in Instr1 == rs in Instr2
What type of circuit implements the == ?
Instruction |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
LD R1, 44(R2) |  |  |  |  |  |  |  |  | 
DADD R5, R1, R7 |  |  |  |  |  |  |  |  | 
DSUB R8, R6, R7 |  |  |  |  |  |  |  |  | 
OR R9, R1, R7 |  |  |  |  |  |  |  |  | 

## Slide 15: Examples of Data Hazards
Dependence
Instruction |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
LD R1, 44(R2) |  |  |  |  |  |  |  |  | 
DADD R5, R6, R7 |  |  |  |  |  |  |  |  | 
DSUB R8, R6, R1 |  |  |  |  |  |  |  |  | 
OR R9, R4, R7 |  |  |  |  |  |  |  |  | 

## Slide 16: Figure C.21 Examples of Data Hazards
Forwarding through the registers
Instruction |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
LD R1, 44(R2) |  |  |  |  |  |  |  |  | 
DADD R5, R6, R7 |  |  |  |  |  |  |  |  | 
DSUB R8, R6, R7 |  |  |  |  |  |  |  |  | 
OR R9, R1, R7 |  |  |  |  |  |  |  |  | 

## Slide 17: Figure C.9 (new slide) Data Forwarding
Copyright © 2011, Elsevier Inc. All rights Reserved.
Figure C.9 The load instruction can bypass its results to the AND and OR instructions, but not to the DSUB, since that would mean forwarding the result in “negative time.”

## Slide 18: Logic to detect Hazards

## Slide 19: Forwarding Figure C.26
Pipeline Reg. Source | Opcode of Source | Pipeline Reg. Destination | Opcode of Destination | Destination of forwarding | Comparison (if equal then forward )

## Slide 20
Pipeline Reg. Source | Opcode of Source | Pipeline Reg. Destination | Opcode of Destination | Destination of forwarding | Comparison (if equal then forward )

## Slide 21: Figure C.23 Forwarding Paths

## Slide 22: Load/Use Hazard

## Slide 23: Delays for Mis-predicted Branches
.

## Slide 24: Figure C.24 Avoiding some Branch Stalls

## Slide 25: Figure FP Latencies

## Slide 26: Figure C.29 MIPS Pipeline +FP Units
.

## Slide 27: Figure C.31 Supporting multiple outstanding FP operations

## Slide 28: Figure C.32 Timings of Independent FP operations
.

## Slide 29: Figure C.33 Stalls due to RAW hazards
.

## Slide 30: Figure C.34 Simultaneous write-back
.

## Slide 35: Figure C.40

## Slide 37: Dynamic Scheduling

## Slide 39: Homework
…

## Slide 40
Figure C.2 The pipeline can be thought of as a series of data paths shifted in time. This shows the overlap among the parts of the data path, with clock cycle 5 (CC 5) showing the steady-state situation. Because the register file is used as a source in the ID stage and as a destination in the WB stage, it appears twice. We show that it is read in one part of the stage and written in another by using a solid line, on the right or left, respectively, and a dashed line on the other side. The abbreviation IM is used for instruction memory, DM for data memory, and CC for clock cycle.

## Slide 41: Figure C.9 (new slide) Data Forwarding
Copyright © 2011, Elsevier Inc. All rights Reserved.
Figure C.9 The load instruction can bypass its results to the AND and OR instructions, but not to the DSUB, since that would mean forwarding the result in “negative time.”

## Slide 42: Figure C-23 Events on Pipeline

## Slide 44
.

## Slide 45: terms interrupt, fault, and exception
The terms interrupt, fault, and exception are used, although not in a consistent fashion. We use the term exception to cover all these mechanisms, including the following:
  I/ O device request Invoking an operating system service from a user program
  Tracing instruction execution
  Breakpoint (programmer-requested interrupt)
  Integer arithmetic overflow FP arithmetic anomaly
  Page fault (not in main memory)
  Misaligned memory accesses (if alignment is required)
  Memory protection violation
  Using an undefined or unimplemented instruction
  Hardware malfunctions
  Power failure

## Slide 46: Linux
File System Hierarchy
Basic Commands
  ls
  cd
  mv
  cp
  rm
  pwd
  gcc
  ./a.out
Editors: emacs, vim, nano, pico, gedit, kate, …

## Slide 47: Linux - lscpu
cocsce-l1d39-16> lscpu
Architecture: x86_64
CPU op-mode(s): 32-bit, 64-bit
Byte Order: Little Endian
CPU(s): 8
On-line CPU(s) list: 0-7
Thread(s) per core: 2
Core(s) per socket: 4
Socket(s): 1
NUMA node(s): 1
Vendor ID: GenuineIntel
CPU family: 6
Model: 60
Stepping: 3
CPU MHz: 800.156
BogoMIPS: 7184.02
Virtualization: VT-x
L1d cache: 32K
L1i cache: 32K
L2 cache: 256K
L3 cache: 8192K
NUMA node0 CPU(s): 0-7

## Slide 48: Man –k ls | grep “^ls”
cocsce-l1d39-16> man -k ls | grep "^ls"
lsattr (1) - list file attributes on a Linux second extended file sy...
lsb (8) - Linux Standard Base support for Debian
lsb_release (1) - print distribution-specific information
lsblk (8) - list block devices
lscpu (1) - display information on CPU architecture
lsdiff (1) - show which files are modified by a patch
lsearch (3) - linear search of an array
lseek (2) - reposition read/write file offset
lshw (1) - list hardware
lsinitramfs (8) - list content of an initramfs image
lsmod (8) - Show the status of modules in the Linux Kernel
lsof (8) - list open files
lspci (8) - list all PCI devices
lspcmcia (8) - display extended PCMCIA debugging information
lspgpot (1) - extracts the ownertrust values from PGP keyrings and li...
lstopo (1) - Show the topology of the system
lstopo-no-graphics (1) - Show the topology of the system
lsusb (8) - list USB devices