## Slide 1: Chapter 13: I/O Systems

## Slide 2: Overview
I/O management is a major component of operating system design and operation
  Important aspect of computer operation
  I/O devices vary greatly
  Various methods to control them
  Performance management
  New types of devices frequent
Ports, busses, device controllers connect to various devices
Device drivers encapsulate device details
  Present uniform device-access interface to I/O subsystem

## Slide 3: I/O Hardware
Incredible variety of I/O devices
  Storage
  Transmission
  Human-interface

## Slide 4: I/O Hardware
Signals between I/O device interface and computer
  Port – physical connection point for device
  Bus - daisy chain or shared direct access
    PCI bus common in PCs and servers, PCI Express (PCIe)
    expansion bus connects relatively slow devices
  Controller (host adapter) – electronics that operate port, bus, device
    Sometimes integrated
    Sometimes separate circuit board (host adapter)
    Contains processor, microcode, private memory, bus controller, etc
      possibly per-device controller with bus controller, microcode, memory, etc

## Slide 5: A Typical PC Bus Structure

## Slide 6: I/O Hardware (Cont.)
I/O instructions control devices
Device Adapters usually have registers
  Command/Status Register (sometime separate)
  Data Register (Data-in / Data-out sometimes separate)
  Address register
  Typically 1-4 bytes, or FIFO buffer
Devices have addresses, used by
  Direct I/O instructions
  Memory-mapped I/O
    Device data and command registers mapped to processor address space
    Especially for large address spaces (graphics)

## Slide 7: Device I/O Port Locations on PCs (partial)

## Slide 8: Polling
For each byte of I/O
  Read busy bit from status register until 0
  Host sets read or write bit and if write copies data into data-out register
  Host sets command-ready bit
  Controller sets busy bit, executes transfer
  Controller clears busy bit, error bit, command-ready bit when transfer done
Step 1 is busy-wait cycle to wait for I/O from device
  Reasonable if device is fast
  But inefficient if device slow
  CPU switches to other tasks?
    But if miss a cycle data overwritten / lost

## Slide 9: Interrupts
Polling can happen in 3 instruction cycles
  Read status, logical-and to extract status bit, branch if not zero
  How to be more efficient if busy for long periods?
CPU Interrupt-request line triggered by I/O device
  Checked by processor after each instruction
Interrupt handler receives interrupts
  Maskable to ignore or delay some interrupts
Interrupt vector to dispatch interrupt to correct handler
  Context switch at start and end
  Based on priority
  Some nonmaskable
  Interrupt chaining if more than one device at same interrupt number

## Slide 10: Interrupt-Driven I/O Cycle

## Slide 11: Intel Pentium Processor Event-Vector Table

## Slide 12: Interrupts (Cont.)
Interrupt mechanism also used for exceptions
  Terminate process, crash system due to hardware error
Page fault executes when memory access error
System call executes via trap to trigger kernel to execute request
Multi-CPU systems can process interrupts concurrently
  If operating system designed to handle it
Used for time-sensitive processing, frequent, must be fast

## Slide 13: End of Part1