## Slide 1: Chapter 10: Mass-Storage Systems

## Slide 2: Chapter 10: Mass-Storage Systems
Overview of Mass Storage Structure
Disk Structure
Disk Attachment
Disk Scheduling
Disk Management
Swap-Space Management
RAID Structure
Stable-Storage Implementation

## Slide 3: Objectives
To describe the physical structure of secondary storage devices and its effects on the uses of the devices
To explain the performance characteristics of mass-storage devices
To evaluate disk scheduling algorithms
To discuss operating-system services provided for mass storage, including RAID

## Slide 4: Overview of Mass Storage Structure
Magnetic disks provide bulk of secondary storage of modern computers
  Drives rotate at 60 to 250 times per second
  Transfer rate is rate at which data flow between drive and computer
  Positioning time (random-access time) is time to move disk arm to desired cylinder (seek time) and time for desired sector to rotate under the disk head (rotational latency)
  Head crash results from disk head making contact with the disk surface
    That’s bad
Disks can be removable
Drive attached to computer via I/O bus
  Busses vary, including EIDE, ATA, SATA, USB, Fibre Channel, SCSI, SAS, Firewire
  Host controller in computer uses bus to talk to disk controller built into drive or storage array

## Slide 5: Moving-head Disk Mechanism

## Slide 6: Magnetic Disks
Platters range from .85” to 14” (historically)
  Commonly 3.5”, 2.5”, and 1.8”
Range from 30GB to 15TB per drive
Performance
  Transfer Rate – theoretical – 6 Gb/sec
  Effective Transfer Rate – real – 1Gb/sec
  Seek time from 3ms to 12ms – 9ms common for desktop drives
  Average seek time measured or calculated based on 1/3 of tracks
  Latency based on spindle speed
    1 / (RPM / 60) = 60 / RPM
  Average latency = ½ latency
(From Wikipedia)

## Slide 7: Magnetic Disk Performance
Access Latency = Average access time = average seek time + average latency
  For fastest disk 3ms + 2ms = 5ms
  For slow disk 9ms + 5.56ms = 14.56ms
Average I/O time = average access time + (amount to transfer / transfer rate) + controller overhead
For example to transfer a 4KB block on a 7200 RPM disk with a 5ms average seek time, 1Gb/sec transfer rate with a .1ms controller overhead =
  5ms + 4.17ms + 0.1ms + transfer time =
  Transfer time = 4KB / 1Gb/s = 32Kb / 1Gb/s = 32b / 1Mb/ms = 32 / (10242) = 0.031 ms
  Average I/O time for 4KB block = 9.27ms + .031ms = 9.301ms

## Slide 8: The First Commercial Disk Drive
1956
IBM RAMDAC computer included the IBM Model 350 disk storage system
5M (7 bit) characters
50 x 24” platters
Access time = < 1 second

## Slide 9: Solid-State Disks
Nonvolatile memory used like a hard drive
  Many technology variations
Can be more reliable than HDDs
More expensive per MB
Maybe have shorter life span
Less capacity
But much faster
Busses can be too slow -> connect directly to PCI for example
No moving parts, so no seek time or rotational latency

## Slide 10: Magnetic Tape
early secondary-storage medium
  Evolved from open spools to cartridges
Relatively permanent and holds large quantities of data
Access time slow
Random access ~1000 times slower than disk

## Slide 11: Magnetic Tape
backup storage or transfer medium
Kept in spool and wound or rewound past read-write head
Once data under head, transfer rates comparable to disk
  140MB/sec and greater
200GB to 1.5TB typical storage
Common technologies are LTO-{3,4,5} and T10000

## Slide 12: Disk Structure
Disk drives 1-dimensional arrays of logical blocks
  the logical block is the smallest unit of transfer
  Low-level formatting creates logical blocks on physical media
array of logical blocks mapped to physical sectors

## Slide 13: Disk Structure
Sector 0: first sector on first track on outermost cylinder
  Mapping proceeds through that track
  then remaining tracks of cylinder
  then remaining cylinders
  Logical to physical address should be easy
    Except for bad sectors
    Non-constant # of sectors per track via constant angular velocity
First Track (outermost cylinder)
Innermost Cylinder

## Slide 14: Disk Attachment
accessed through I/O ports talking to I/O busses
Direct to host: SCSI bus
  up to 16 devices on one cable
  SCSI initiator requests operation and SCSI targets perform tasks
  Each target can have up to 8 logical units (disks attached to device controller)
Storage Area Networks
  Fibre Channel: high-speed serial architecture
  fabric: FCs working in unison

## Slide 15: Storage Array
Storage Array
  Ports to connect hosts to array
  Memory, controlling software (sometimes NVRAM, etc)
  A few to thousands of disks
  RAID, hot spares, hot swap (discussed later)
  Shared storage -> more efficiency

## Slide 16: Storage Area Network
Common in large storage environments
Multiple hosts attached to multiple storage arrays - flexible

## Slide 17: Storage Area Network (Cont.)
SAN
  one or more storage arrays
  Connected to one or more Fibre Channel switches
  Hosts also attach to the switches
  Easy to add/remove storage
  Easy to add new host
  Low-latency Fibre Channel fabric

## Slide 18: Network-Attached Storage
Network-attached storage (NAS):
  available over a network (instead of a bus)
  Remotely attachment to file systems
  NFS and CIFS are common protocols
  Access via remote procedure calls (RPCs)
iSCSI protocol uses IP network to carry the SCSI protocol
  Remote attachment to devices (blocks)

## Slide 19: Disk Scheduling
The operating system is responsible for using hardware efficiently
  use drives efficiently,
   fast access time
   good disk bandwidth
Disk bandwidth: bytes transferred / elapsed time
Elapsed time: time from request to completion
Minimize seek time
Seek time  seek distance

## Slide 20: Disk Scheduling (Cont.)
There are many sources of disk I/O request
  OS
  System processes
  Users processes
I/O request parameters:
  includes input or output mode,
  disk address,
  memory address,
  number of sectors to transfer

## Slide 21: Disk Scheduling (Cont.)
OS maintains queue of requests, per disk or device
Idle disk can immediately work on I/O request, busy disk means work must queue
  Optimization algorithms only make sense when a queue exists
Note: drive controllers have small buffers to hold queue of I/O requests (of varying “depth”)

## Slide 22: Disk Scheduling (Cont.)
Several algorithms exist to schedule the servicing of disk I/O requests
The analysis is true for one or many platters
We illustrate scheduling algorithms with a request queue (0-199)
98, 183, 37, 122, 14, 124, 65, 67
Head pointer 53

## Slide 23: FCFS
Illustration shows total head movement of 640 cylinders

## Slide 24: SSTF
Shortest Seek Time First selects the request with the minimum seek time from the current head position
SSTF scheduling is a form of SJF scheduling; may cause starvation of some requests
Illustration shows total head movement of 236 cylinders

## Slide 25: SSTF (Cont.)

## Slide 26: SCAN
SCAN:
  start at one end of the disk
  moves toward the other end
  servicing requests until it gets to the other end of the disk
  reversed direction and continue.
SCAN algorithm Sometimes called the elevator algorithm
Illustration shows total head movement of 208 cylinders

## Slide 27: SCAN (Cont.)

## Slide 28: C-SCAN
More uniform wait time than SCAN
C-SCAN:
  start at one end of the disk
  moves toward the other end
  servicing requests until it gets to the other end of the disk
  Return to beginning of disk immediately
Treats the cylinders as a circular list that wraps around from the last cylinder to the first one
Total number of cylinders?

## Slide 29: C-SCAN (Cont.)

## Slide 30: C-LOOK
Improvements: Don’t go all the way to the last/first cylinder unless there is a request there
SCAN  LOOK
C-SCAN  C_LOOK
Total number of cylinders?

## Slide 31: C-LOOK (Cont.)

## Slide 32: Selecting a Disk-Scheduling Algorithm
SSTF is common and has a natural appeal
SCAN and C-SCAN perform better for systems that place a heavy load on the disk
  Less starvation
Performance depends on the number and types of requests
Requests for disk service can be influenced by the file-allocation method
  And metadata layout

## Slide 33: Selecting a Disk-Scheduling Algorithm
How to select a scheduling algorithm?
  should be a separate module
  Easy to replace if needed
Either SSTF or LOOK good choices
What about rotational latency?
  Note: We’ve focused on seek time only
  Difficult for OS to calculate
How does disk-based queueing effect OS queue ordering efforts?

## Slide 34: Disk Management
Physical formatting — Dividing a disk into sectors
  Each sector can hold:
    Header information
    Data
    Error correction code (ECC)
  Usually 512 bytes of data
OS needs to store its own data structures to disk
  Partition: a logical disk comprised of a set of cylinders
  Logical formatting or “making a file system”
  Efficiency: group blocks into clusters
    Disk I/O done in blocks
    File I/O done in clusters

## Slide 35: Disk Management
Other Sundries:
  Raw disk access: Apps such as databases
  Boot block initializes system
    The bootstrap is stored in ROM
    Bootstrap loader program stored in boot blocks of boot partition
  Methods such as sector sparing used to handle bad blocks

## Slide 36: Booting from a Disk in Windows

## Slide 37: Virtual Memory: Swap-Space
Swap-space — used as extension of main memory
  Less common now due to memory capacity increases
  carved out of the normal file system
  usually a separate disk partition (raw)

## Slide 38: Virtual Memory: Swap-Space
Swap-space management
  4.3BSD allocated when process starts
    holds text segment (the program) and data segment
  Kernel uses swap maps to track swap-space use
  Solaris 2 uses lazy allocation:
    only when a dirty page is forced out of physical memory
    not when the virtual memory page is created
    File data written to swap space until write to file system requested
    Other dirty pages go to swap space due to no other home
    Text segment pages thrown out and reread from the file system as needed

## Slide 39: Virtual Memory: Swap-Space
What if a system runs out of swap space?
Some systems allow multiple swap spaces

## Slide 40: Data Structures for Swapping on Linux Systems

## Slide 41: RAID Structure
RAID – Redundant Array of Inexpensive Disks
  reliability via redundancy
Increase the mean time to failure
Mean time to repair – exposure time when another failure could cause data loss
Mean time to data loss based on above factors

## Slide 42: RAID (Cont.)
Use multiple disks cooperatively:
Disk striping: a group of disks act as one storage unit
RAID schemes improve performance and improve the reliability of the storage system by storing redundant data
  Mirroring or shadowing (RAID 1) keeps duplicate of each disk
  Striped mirrors (RAID 1+0) or mirrored stripes (RAID 0+1) provides high performance and high reliability

## Slide 43: RAID (0 + 1) and (1 + 0)

## Slide 44: RAID (Cont.)
Block interleaved parity (RAID 4, 5, 6) uses much less redundancy
RAID within a storage array can still fail if the array fails, so automatic replication of the data between arrays is common
Frequently, a small number of hot-spare disks are left unallocated, automatically replacing a failed disk and having data rebuilt onto them

## Slide 45: RAID Levels

## Slide 46: Other Features
Snapshot is a view of file system before a set of changes take place (i.e. at a point in time)
  More in Ch 12
Replication is automatic duplication of writes between separate sites
  For redundancy and disaster recovery
  Can be synchronous or asynchronous
Hot spare disk
  automatically used by RAID if a disk fails
  replaces failed disk and rebuild the RAID set if possible
  Decreases mean time to repair

## Slide 47: End of Chapter 10