Visual - Inertial Navigation, Mapping and Localization: A Scalable Real-Time Causal Approach
Eagle S. Jones
Stefano Soatto
Presented by Sean Doherty

---
Introduction
- Monocular vision and inertial measurements
- Possible to estimate unknown gravity vector and unknown transformation between camera and inertial unit
- Everything handled on-line
- Requires a “rich enough” motion sequence
- Vision presents a natural complement to inertial sensors

---
Outline
- Ego-motion Estimation
- Implementation
- Open-loop Navigation Experiments
- Map Building and Localization
- Conclusion

---
Ego-Motion
- Notation follows a fairly standard pattern described in detail in (Murray et al., 1994) or (Ma et al., 2003).
- Fundamental representation of motion of a rigid body:
R in SO(3)
T in setR ^3
g = left [ matrix{R # T ## 0 # 1} right ]
g = ( R,T ) in SE( 3 )

---
Ego-Motion (cont.)
- Denote the coordinates of point i in the inertial frame:
- Denote the projection of point i onto the (moving) image plane:
- Ideal vision algorithm would use the model:
  and maintain correspondence and overcome occlusions

---
General Motion/State Model

---
Observability: Indistinguishable trajectories
- When only inertial measurements are available, the model is not observable.
- Consider an output trajectory for yimu(t) generated from a particular acceleration a(t). We integrate the model to obtain:
  and we can immediately see that any initial velocity will give rise to the same exact output trajectory. Hence, from the output, we will never be able to determine the translational velocity, and therefore the position of the body frame, uniquely.
v( t ) = int from{0} to{t} a( T ) dT + v_i

---
Observability of camera-to-inertial calibration
- Requires “sufficiently exciting” motion:
  - Non-zero linear acceleration
  - Non-constant rotational axis
- Treated as a separate thread filter problem

---
Observability of unknown gravity vector
- Dealing with gravity is an art of the inertial navigation community
- Approach here integrates visual and inertial measurements and is added to the model with trivial dynamics and small model error covariance.
- This parameter has the same “sufficiently exciting” motion restraint as the calibration

---
Outline
- Ego-motion Estimation
- Implementation
- Open-loop Navigation Experiments
- Map Building and Localization
- Conclusion

---
Discretization
- IMU produces readings at 100Hz while monocular camera produces images at 30Hz
  - Handled by introducing a time step, dt, and multiplying the process noises by dt at each prediction step
  - Our state can now be updated asynchronously as different measurements become available.

---
Discretization
- Hardware (sensors) have non-deterministic delays that are variable between different sensors and interfaces
- Taking into account the fluctuation of the delay requires dedicated hardware with individual time-stamps
- We forgo this by only compensating each measurement by the average delay

---
Autocalibration and Normal Operation
- Requirements may not be achieved during scenarios of interest
- Calibration does not change significantly over time
- Therefore, use a manual switch to change between normal operation and “auto-calibration sequence”

---
Auto-calibration Sequence
Described as “sufficiently complex sequence” in the paper with little more detail

---
Handling of Missing and New Data
- Groups – set number (N) of point features simultaneously selected
- Represent each group with N+6 states opposed to tracking N features each having multiple states.
  - Log-depths
  - Six states representing the position and orientation of the group relative to the best estimate of ego-motion at time t.
- Tracking drift is relatively small because groups are only being successfully tracked for a range typically between 10 and 30 frames

---
More precise
- Let g(Tj) = gsb(Tk) be the transformation mapping the body frame to the spatial frame
  - Let j be our reference group
    - The reference for our initial group would be T(0)=0 and Ω(0)=0
    - As soon as all features in our reference group have been lost, it is necessary to choose another group as a reference, and to fix its reference frame:
      - Tjref=T(tj) and Ωjref=Ω(tj) for the reference group j captured at time t
      - Our transformation mapping the reference frame (body frame) to the spatial frame (IMU reference frame at t = 0) becomes:
        g(Tj) = gjref=(Rjref,Tjref)=(e , Tjref)
      - Our transformation mapping the camera reference frame (when the point first appeared) to the current camera frame becomes:
        gtot=gcb g(t)-1 gjref gcb-1 = (Rtot, Ttot)
func e^{Ω^{j}_ref}
Ω^{j}_{ ref }

---
Model with reference

---
Open-loop Navigation Experiments
- Ego-motion Estimation
- Implementation
- Open-loop Navigation Experiments
- Map Building and Localization
- Conclusion

---
Open-loop Navigation Experiments

---
Open-loop Navigation Experiments
- 10 minute sequence
- Rectangle traversed twice (total length of 570m)
- Overlayed blueprint of building

---
Open-loop Navigation Experiments
- Outdoor loop with low evening sun and rush hour traffic
- 7.9km in 16.5 minutes
- Revisited a position 5,808m after its initial visit

---
Open-loop Navigation Experiments
- Much longer outdoor loop: 30.3km in 62 minutes
- At this scale of time and distance the rotation and curvature of the earth result in non-negligible errors.
- Could be easily handled (substantially reduced) by the model by adding terms but doesn't emphasize the generalness and robustness of this algorithm

---
Outline
- Ego-motion Estimation
- Implementation
- Open-loop Navigation Experiments
- Map Building and Localization
- Conclusion

---
Map Building and Localization
- Features lost are removed from the state and stored in memory together with their position in the global reference frame as well as with a descriptor of the local photometry around the tracked feature
- Constitutes a map that can be used for localization using standard tools of multiple-view geometry.
- Complexity of map grows rapidly, and therefore visual features must be organized efficiently in order to enable rapid localization

---
Mapping Module
Constructs a graph based on the output of the structure from motion filter → exploit structural constraints provided by the map for location matching

---
Short Laboratory Graph

---
Short Laboratory Graph (with geometric constraints)

---
Loop Closure
As the map is being built, every new location is checked against the entire map, thus creating the loop closure echanism. Scoring function for nodes is based on the inverse document frequency.

---
Conclusion
- System for estimating the motion of a sensing platform for which the system can operate with initialing unkown calibration and gravity vector.
- Has the ability to build maps and recongnize previously seen locations in the map in real-time in a scalable fashion.